## Slide 1: Handoff Delay for 802.11b Wireless LANs
Masters Project defense
Anshul Jain
Committee:
Dr. Henning Schulzrinne, Columbia University
Dr. Zongming Fei, University of Kentucky
Dr. Jim Grffioen, University of Kentucky
Dr. Ken Calvert, University of Kentucky

## Slide 2: Overview
The IEEE 802.11 Wireless LAN architecture
Channel Allocation
802.11 Management Frames
Handoff Procedure
Experimental Setup
Configuration Problems
Details of Experiments
Summary of Experiments
Conclusion

## Slide 3: The IEEE 802.11 Wireless LAN architecture
Wireless LAN Station (STA)
Access Points (AP)
Basic Service Set (BSS)
Distribution System (DS)
Extended Service Set (ESS)

## Slide 4: The IEEE 802.11 Wireless LAN architecture (cont.)
Two different ways to configure a network
  Ad-hoc
    No structure
    Every node can talk to each other
  Infrastructure
    Fixed APs with which mobile nodes can communicate
    APs are connected to DS

## Slide 5: Channel Allocation
83.5 MHz from 2.4000 GHz to 2.4835 GHz
11 channels, each channel being 22 MHz in width, and each channel centered at 5 MHz intervals

## Slide 6: 802.11 Management Frames
Authentication
Deauthentication
Association request
Association response
Reassociation request
Reassociation response
Disassociation
Beacon
Probe request
Probe response

## Slide 7: Handoff Procedure
Mobile node moves from coverage area of one AP to that of another AP
Steps During Handoff
  Discovery
    Initiation and scanning phase
    Active and passive scanning mode
  Reauthentication
    Authentication and re-association

## Slide 8: Handoff Procedure (cont.) Active Scanning Mode procedure
Transmit a probe request frame which contains the broadcast address as the destination.
Start a probe timer.
Listen for probe response.
If no response received by minChannelTime, scan next channel.
If one or more responses are received by minChannelTime, stop accepting probe responses at maxChannelTime and process all received responses.
Move to next channel and repeat above steps.

## Slide 9: Handoff Procedure (cont.)
Sequence of messages exchanged between the mobile node and the participating APs.
  Probe
  Authentication
  Reassociation

## Slide 10: Experimental Setup
Hardware Specification
  Wireless Network
    Laboratory of Advanced Networking at University of Kentucky
    Deployed network named Anshul with APs on channel 1 and 11
  Wireless Client
    Pentium III 300 MHz, 256 MB RAM Gateway laptop with Cisco Aironet 350 wireless card
  Wireless Sniffer Systems
    Pentium IV 1.67 GHz, 256 MB RAM Sony laptop with Linksys WPC11 v3.0 wireless PCMCIA card
    Pentium III 300 MHz, 128 MB RAM IBM laptop with Linksys WPC11 v3.0 wireless card

## Slide 11: Experimental Setup (cont.)
Software Specification
  Operating System
    Red Hat 8.0 with kernel version 2.4.18-14
    Windows XP
  Drivers
    Driver used for Cisco 350 card is airo-linux
    Driver used for Linksys WPC11 card is linux-wlan-ng-0.1.16.pre10
  Software Tools
    Kismet 802.11 wireless network sniffer
    Wilpacket’s AiroPeek packet analyzer
    Ethereal network protocol analyzer
    Cisco Aironet Client Utility

## Slide 12: Configuration Problems
The Cisco drivers downloaded from Cisco’s website do not support promiscuous mode
Using Kismet, one can’t restrict Cisco 350 cards to sniff on one particular channel
With Cisco cards, no current drivers on linux reports signal strength correctly
Monitor mode precludes the ability of the wireless card to send data to the network
Each vendor has their own formula to convert RSSI value to Decibel Milliwatts (dBm). Could not find this conversion formula for Linksys.

## Slide 13: Details of Experiments
Experiments are divided into the following categories:
Handoff analysis when APs having different SSIDs are on different channels
Handoff analysis when APs having different SSIDs are on the same channel
Handoff analysis when APs having the same SSID are on different channels
Handoff analysis when APs having the same SSID are on the same channel
Effect of Beacon Interval on handoff Latency
Signal strength at the point of handoff

## Slide 14: APs having different SSIDs on different channels

## Slide 15: Probe Delay Calculation
Expected
Channel 1:
  37ms delay for AP Anshul-2
  17ms delay for AP Anshul-1
  Total of 54ms
Channel 2-10:
  17ms delay for AP Anshul-2
  17ms delay for AP Anshul-1
  Total of 306ms
Channel 11:
  17ms delay for AP Anshul-2
  37ms delay for AP Anshul-1
  Total of 54ms
Total: 414ms

## Slide 16: Results and Analysis
Average handoff delay: 531.6ms
Average probe delay: 528ms
Average authentication delay: 1.3ms
Average reassociation delay: 2.3ms
95% Confidence Interval: 516.1ms to 547.106ms

## Slide 17: Why is this discrepancy?
APs overhearing Probe Request due to channel overlapping
Sending Probe Response back
AP on channel 1 sends Probe Response for Probe Requests on channel 2,3 and 4
AP on channel 11 sends Probe Response for Probe Requests on channel 8,9 and 10

## Slide 18: Probe Delay Calculation
Channel 1:
  37ms delay for AP Anshul-2
  17ms delay for AP Anshul-1
  Total of 54ms
Channel 2-4:
  37ms delay for AP Anshul-2
  17ms delay for AP Anshul-1
  Total of 162ms
Channel 5-7:
  17ms delay for AP Anshul-2
  17ms delay for AP Anshul-1
  Total of 102ms
Channel 8-10:
  17ms delay for AP Anshul-2
  37ms delay for AP Anshul-1
  Total of 162ms
Channel 11:
  17ms delay for AP Anshul-2
  37ms delay for AP Anshul-1
  Total of 54ms
Total: 534ms

## Slide 19: APs having different SSIDs on same channel

## Slide 20: Probe Delay Calculation
Channel 1-7:
  17ms delay for AP Anshul-2
  17ms delay for AP Anshul-1
  Total of 238ms
Channel 8-10:
  37ms delay for AP Anshul-2
  37ms delay for AP Anshul-1
  Total of 222ms
Channel 11:
  37ms delay for AP Anshul-2
  37ms delay for AP Anshul-1
  Total of 74ms
Total: 534ms

## Slide 21: Results and Analysis
Average handoff delay: 532ms
Average probe delay: 528.4ms
Average authentication delay: 1.3ms
Average reassociation delay: 2.3ms
95% Confidence Interval: 510.306ms to 553.694ms

## Slide 22: APs having same SSID on different channels

## Slide 23: Probe Delay Calculation
Channel 1:
  37ms delay for AP Anshul
  Total of 37ms
Channel 2-4:
  37ms delay for AP Anshul
  Total of 111ms
Channel 5-7:
  17ms delay for AP Anshul
  Total of 51ms
Channel 8-10:
  37ms delay for AP Anshul
  Total of 111ms
Channel 11:
  37ms delay for AP Anshul
  Total of 37ms
Total: 347ms

## Slide 24: Results and Analysis
Average handoff delay: 329.4ms
Average probe delay: 325.8ms
Average authentication delay: 1.3ms
Average reassociation delay: 2.3ms
95% Confidence Interval: 318.303ms to 340.497ms

## Slide 25: APs having same SSID on same channel

## Slide 26: Probe Delay Calculation
Channel 1-7:
  17ms delay for AP Anshul
  Total of 119ms
Channel 8-10:
  37ms delay for AP Anshul
  Total of 111ms
Channel 11:
  37ms delay for AP Anshul
  Total of 37ms
Total: 267ms

## Slide 27: Results and Analysis
Average handoff delay: 269.7ms
Average probe delay: 266.1ms
Average authentication delay: 1.3ms
Average reassociation delay: 2.3ms
95% Confidence Interval: 258.564ms to 280.836ms

## Slide 28: Effect of Beacon Interval on handoff Latency
Note: APs have same SSID and are on different channels

## Slide 29: Results and Analysis
Average handoff delay: 306.2ms
Average probe delay: 302.6ms
Average authentication delay: 1.3ms
Average reassociation delay: 2.3ms

## Slide 30: Signal strength at the point of handoff

## Slide 31: Results and Analysis
Average signal strength: -79.5dBm
RSSI: 32%
95% Confidence Interval: -81.926dBm to -77.074dBm

## Slide 32: Summary of Experiments

## Slide 33: Conclusion
Probe delay accounts for more than 99% of overall handoff latency
Significant variation in handoff latency with change in APs SSID and channel
Smallest handoff latency when APs have same SSID and are on same channel
Changing the signal strength threshold does not effect handoff latency
Beacon interval has no effect on handoff latency
Handoff latencies we measured far exceed the guidelines for jitter in voice over IP applications where the overall latency is recommended not to exceed 50ms